## Slide 1: ElectroPsych (EPsych) Matlab Toolbox
http://epsych.googlecode.com
by Daniel Stolzberg

## Slide 2
Real-time control of stimuli and behavioral apparatus
Precise event timestamps for pairing with electrophysiology
High quality signal generation and acquisition
Experiment Parameterization
Complete trial-by-trial parameterization based on custom Matlab functions
Signal Calibration
Modular design allows customizable functionality
Custom RPvds circuit macros for behavior real-time behavior control
EPsych
Easy scripting/debugging
Huge library of functions and toolboxes available

## Slide 3
Define hardware and RPvds circuits
Parameterize experiments
Custom trial-selection function for dynamic experiments (optional)
Runs behavior/electrophysiology experiment by controlling OpenEx and trial-by-trial stimulus parameters
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Create real-time components for signal generation and data acquisition
Integrates with TDT OpenEx software
Behavioral hardware input/output
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Basic Workflow

## Slide 4
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Designing RPvds Circuits for EPsych

## Slide 5
Custom RPvds Macros
Behavior Paradigms
Signal Calibration
Cross-module Synchronous Trigger
(ep_EPhys)

## Slide 6
Custom RPvds Macros
Stimulus Detection Tasks
Controls timing of basic stimulus detection behavior paradigm.
One circuit per subject
When InhibitTrial is true, the macro is inhibited. In other words, if TTL goes high while InhibitTrial is high then nothing happens.
  Can be used for a timeout or to institute a mandatory inter-trial interval.
The RespLatency output is the time since the end of the RespWinDelay period until the TTL goes low or the RespWinDur expires.
The sampling rate being used in the RPvds must be selected using the setup tab.

## Slide 7
Custom RPvds Macros
Two-Alternative Forced Choice Tasks
Controls timing of basic Two-Alternative Forced Choice behavior paradigm.
One circuit per subject
When InhibitTrial is true, the macro is inhibited. In other words, if TTL goes high while InhibitTrial is high then nothing happens.
  Can be used for a timeout or to institute a mandatory inter-trial interval.
Trial is over when either TTL_A or TTL_B goes high. The first of these two to go high is maintained until trial is reset.
The RespLatency output is the time since the end of the RespWinDelay period until the TTL_A or TTL_B goes high or the RespWinDur expires.
The sampling rate being used in the RPvds must be selected using the setup tab.

## Slide 8
Custom RPvds Macros
Signal Calibration

## Slide 9
Custom RPvds Macros
Cross-module Synchronous Trigger
(ep_EPhys)

## Slide 10
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Parameterizing Experiments

## Slide 11
Define TDT hardware module types
ep_ExperimentDesign
Parameterizing Experiments

## Slide 12
Define parameter values, functions, and calibrations
ep_ExperimentDesign
Parameterizing Experiments

## Slide 13
Relates to parameter tags in RPvds circuits
ep_ExperimentDesign
Parameterizing Experiments

## Slide 14
Determines functionality of the parameter.
Typically “Write/Read” is appropriate.
ep_ExperimentDesign
Parameterizing Experiments

## Slide 15
Specify values for each (‘write’) parameter.
Express as a number, numbers, or Matlab expression
Use two values and check the “Rand” box to generate a new value for each trial selected from a randomized uniform distribution bounded by the values
ep_ExperimentDesign
Parameterizing Experiments

## Slide 16
Associate parameter values together
ep_ExperimentDesign
Parameterizing Experiments

## Slide 17
Check to use WAV files or data buffers as values for the parameter.
ep_ExperimentDesign
Parameterizing Experiments

## Slide 18
Associate a calibration file with parameter values
File is created using the calibration utility (ep_CalibrationUtil) or a manually created file.
ep_ExperimentDesign
Parameterizing Experiments

## Slide 19
Operational Trigger
Unchecked
The next trial is presented automatically
Typical stimulus presentation
# Reps determines how many presentations of each individual stimulus will be delivered
ITI is the inter-trigger-interval (in milliseconds). If two values are specified (ex: 1000 2000) then a random ITI will be generated between the two values (from a uniform distribution).
Checked
Wait for a trigger to run the next trial
Behavioral experiments in which the subjects initiates its own trials
Electrophysiology experiments in which the user presses a button (ex: physical button attached to a digital line on hardware; click a button in a Matlab GUI; spike-triggered stimulus; etc)
ep_ExperimentDesign
Parameterizing Experiments

## Slide 20
ep_ExperimentDesign
Parameterizing Experiments
Trial-Select Function (optional)
Specify a custom Matlab function to select each trial.
Function must be on the Matlab path.
Function must have one input and one output.
Function Prototype:
function NextTrialID = MyCustomFunction(TRIALS)
See the help for the default function for instructions on how to create a custom trial-select function
>> help DefaultTrialSelectFcn

## Slide 21
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Running an Experiment

## Slide 22
Electrophysiology
ep_EPhys
Behavior / Behavior & Electrophysiology
ep_RunExpt

## Slide 23
http://tortoisesvn.net/
Obtaining and Updating EPsych
Install whatever is the latest version for your computer (typically 64-bit)

## Slide 24
Installation
Navigate to target directory in Windows Explorer.
  Recommended: ‘c:/MATLAB/work/’
Right-click in empty area within Windows Explorer.
Click “SVN Checkout…”
  URL of Repository: https://epsych.googlecode.com/svn/trunk/
  Checkout Directory: C:\MATLAB\work\epsych (or wherever)
  Click OK
  If successful, you should see folders and files being downloaded from the internet.

## Slide 25
Updating
Right-click “epsych” folder in Windows Explorer.
Click “SVN Update”
You should see a list of files being updated.

## Slide 26
GUIs
Calibration of stimuli … ep_CalibrationUtil
Display Preferences … ep_DisplayPrefs
Generate Bitmasks … ep_DisplayPrefs
Helpful Functions
Retrieve Tank Data … TDT2mat
TDT to Plexon (PLX) … TDT2PLX
Plexon to TDT … PLX2TDT
Resources
Examples ..\epsych\.examples
RPvds Macros ..\epsych\.circuit_macros
Integration with MySQL Database ..\epsych\database
Uploading … DB_UploadUtility
Accessing/Browsing … DB_Browser
Other Stuff

## Slide 27
Spike Sorting
Tank
Upload to Database
DB_UploadUtility
Database Browser & Analysis
DB_Browser
MySQL Database

## Slide 28
MySQL Database