## Slide 1: ElectroPsych (EPsych) Matlab Toolbox
http://epsych.googlecode.com
by Daniel Stolzberg

## Slide 2
Real-time control of stimuli and behavioral apparatus
Precise event timestamps for pairing with electrophysiology
High quality signal generation and acquisition
Experiment Parameterization
Complete trial-by-trial parameterization based on custom Matlab functions
Signal Calibration
Modular design allows customizable functionality
Custom RPvds circuit macros for behavior real-time behavior control
EPsych
Easy scripting/debugging
Huge library of functions and toolboxes available

## Slide 3
Define hardware and RPvds circuits
Custom trial-selection function for dynamic experiments (optional)
Runs behavior/electrophysiology experiment by controlling OpenEx and trial-by-trial stimulus parameters
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Create real-time components for signal generation and data acquisition
Integrates with TDT OpenEx software
Behavioral hardware input/output
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Basic Workflow

## Slide 4
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Designing RPvds Circuits for EPsych

## Slide 5
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Custom RPvds Macros
Custom RPvds Macros
(../epsych/.circuit_macros)

## Slide 6
Custom RPvds Macros
Behavior Paradigms
Signal Calibration
Cross-module Synchronous Trigger
(ep_EPhys)

## Slide 7
Custom RPvds Macros
Stimulus Detection Tasks
Controls timing of basic stimulus detection behavior paradigm.
One circuit per subject
When InhibitTrial is true, the macro is inhibited. In other words, if TTL goes high while InhibitTrial is high then nothing happens.
  Can be used for a timeout or to institute a mandatory inter-trial interval.
The RespLatency output is the time since the end of the RespWinDelay period until the TTL goes low or the RespWinDur expires.
The sampling rate being used in the RPvds must be selected using the setup tab.

## Slide 8
Custom RPvds Macros
Two-Alternative Forced Choice Tasks
Controls timing of basic Two-Alternative Forced Choice behavior paradigm.
One circuit per subject
When InhibitTrial is true, the macro is inhibited. In other words, if TTL goes high while InhibitTrial is high then nothing happens.
  Can be used for a timeout or to institute a mandatory inter-trial interval.
Trial is over when either TTL_A or TTL_B goes high. The first of these two to go high is maintained until trial is reset.
The RespLatency output is the time since the end of the RespWinDelay period until the TTL_A or TTL_B goes high or the RespWinDur expires.
The sampling rate being used in the RPvds must be selected using the setup tab.

## Slide 9
Custom RPvds Macros
Signal Calibration

## Slide 10
Custom RPvds Macros
Cross-module Synchronous Trigger
(ep_EPhys)

## Slide 11
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Parameterizing Experiments

## Slide 12
Define TDT hardware module types
ep_ExperimentDesign
Parameterizing Experiments

## Slide 13
Define parameter values, functions, and calibrations
ep_ExperimentDesign
Parameterizing Experiments

## Slide 14
Operational Trigger
Unchecked
The next trial is presented automatically
Typical stimulus presentation
# Reps determines how many presentations of each individual stimulus will be delivered
ITI is the inter-trigger-interval (in milliseconds). If two values are specified (ex: 1000 2000) then a random ITI will be generated between the two values (from a uniform distribution).
Checked
Wait for a trigger to run the next trial
Behavioral experiments in which the subjects initiates its own trials
Electrophysiology experiments in which the user presses a button (ex: physical button attached to a digital line on hardware; click a button in a Matlab GUI; spike-triggered stimulus; etc)
ep_ExperimentDesign
Parameterizing Experiments

## Slide 15
ep_ExperimentDesign
Parameterizing Experiments
Trial-Select Function (optional)
Specify a custom Matlab function to select each trial.
Function must be on the Matlab path.
Function must have one input and one output.
Function Prototype:
function NextTrialID = MyCustomFunction(TRIALS)
See the help for the default function for instructions on how to create a custom trial-select function
>> help DefaultTrialSelectFcn

## Slide 16
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Behavior/Electrophysiology
ep_RunExpt/ep_EPhys
Running an Experiment

## Slide 17
Defines hardware and RPvds circuits
One or multiple experiment protocol files can be made for each behavioral box
Custom trial-selection function for dynamic experiments (optional)
Defines which subject is assigned to which behavioral box
User-defined configuration for how to display and graph subject performance during the experiment
Customizable functions for full control over experiment during runtime (optional)
Runs Behavioral experiment with or without TDT OpenEx software for electrophysiology
RPvds Circuit
RPvds Circuit
RPvds Circuit
RPvds Circuit
TDT RPvds Software
(*.rcx)
Create real-time components for signal generation and data acquisition
Behavioral hardware input/output
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
Experiment Protocol
ep_ExperimentDesign
(*.prot)
Run-Time
ep_RunExpt
(*.config)
Paradigm Contingencies & Display
ep_DisplayPrefs
(*.epdp)
Basic Workflow

## Slide 18
Electrophysiology
ep_EPhys
Behavior / Behavior & Electrophysiology
ep_RunExpt